## Slide 1: Wireless Tremor Detection
ME 505 Group 3
Sadra Hemmati, Nav Kikkeri, Carter McVeigh, Nolan Perry

## Slide 2: Background
Problem at hand:
  Many infants are exposed to illicit drugs during development
  They may experience withdrawal
  Symptoms include violent tremors which may injure the child
Task
  We have to develop a device which can wirelessly monitor a child’s motion
  It must alert nurses if there are any tremors
  The system must be simple and easy to use

## Slide 3: Completed Work
Proof of Concept
  Acquired and integrated the hardware to create a testbed device
    Device is able to differentiate between normal body movements and tremors
  Designed a printed circuit board
  Developed iOS app which would use Bluetooth Low Energy to receive data and present textual indication
Further Development
  Integrate all hardware onto wireless prototype (accelerometer)
  Apple Developer’s Account

## Slide 4: Solution
Our Wired Design
    Low power microprocessor – RFDuino, which has a Bluetooth low energy transceiver
    Integrated into developer kit with USB programming dongle
    Large accelerometer (easy to solder)
Why?
  Simpler layout before minimizing space
  Easily verify and develop Arduino code

## Slide 5: Solution
Our Wireless Design
  low power microprocessor – RFDuino, which has a Bluetooth low energy tranceiver
  Accelerometer
  All mounted on a PCB
  Approximate total weight – 7 grams
Why?
  Simple to use devices
  Minimize size and power requirements
  Accelerometer must sample at an appropriate rate

## Slide 6: Hardware Components
Component | Why?
RFDuino developer kit, with a RFDuino and USB Programming dongle | Primary test bed for project development. Has built in RFDuino, Bluetooth transceiver, and USB port for fast programming. Used to verify concept
RFDunio Microprocessor (RFD22301) | Has an integrated Bluetooth low energy transceiver. Low power, with peak power draw at 12mA. Has range of 30 feet. Meets minimum processing speeds.
Accelerometer | Has a sampling rate of .5Hz – 1kHz, and consumes 10uA.
110mAh Li-Ion battery | Supplies power to the device for 9+ hours. Compact size. Rechargeable.

## Slide 7: Our Design

## Slide 8: Our PCB Design

## Slide 9: Tremor Detection
Differentiates between tremors and general movements
Accelerometer is sampled at 50Hz
Algorithm:
  Reads 30 samples
  Average is taken
  Compares each successive sets of data with the average
  Counts the number of times the acceleration crosses the average

## Slide 10: Acceleration Data
Chart: Acceleration - No Motion
X | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2 | -0.2
Y | -0.4 | -0.4 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.4 | -0.5 | -0.4 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.4 | -0.4 | -0.4 | -0.4 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.4 | -0.4 | -0.4 | -0.5 | -0.5 | -0.5 | -0.5 | -0.4 | -0.4 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5 | -0.5
Z | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.7 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.7 | 0.8 | 0.8 | 0.8 | 0.8 | 0.7 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8

## Slide 11: Acceleration Data
Chart: Acceleration - Natural Motion

## Slide 12: Acceleration Data
Chart: Acceleration - Tremors
Y | -0.2 | 0.2 | 0 | -0.1 | -0.3 | -0.8 | -0.4 | 0 | 0.2 | 0.1 | 0 | 0 | -0.2 | -0.3 | -0.2 | 0.1 | 0 | -0.2 | -0.4 | -0.3 | -0.4 | 0.2 | 0.1 | 0.1 | -0.3 | -0.5 | -0.3 | 0 | 0 | -0.1 | -0.3 | -0.3 | 0 | 0 | -0.2 | -0.2 | -0.2 | -0.1 | -0.1 | -0.1 | -0.5 | 0 | 0 | 0 | -0.2 | -0.4 | -0.3 | -0.3 | 0 | 0.3 | -0.3 | 0 | 0.3 | 0 | -0.4 | -0.7 | -0.5 | 0 | 0.4 | -0.1
Z | 0.7 | 0.8 | 1.1 | 1.5 | 1.1 | 0.6 | 0.1 | 0.7 | 1.1 | 1.3 | 0.8 | 0.8 | 1 | 1.2 | 1.1 | 0.6 | 0.7 | 0.8 | 1.1 | 1.1 | 0.8 | 0.6 | 1 | 1.2 | 1.1 | 1 | 0.8 | 0.9 | 0.9 | 1.1 | 1 | 0.8 | 0.7 | 0.8 | 1 | 1.1 | 1 | 0.9 | 0.8 | 0.9 | 0.8 | 0.7 | 1 | 1 | 1 | 0.9 | 0.9 | 0.9 | 1 | 1 | 0.9 | 0.8 | 0.7 | 0.9 | 1 | 1.1 | 1 | 0.7 | 0.9 | 0.9

## Slide 13: UI Design
We explored different options
  Android – did not have necessary OS updates to access BLE
  Windows/Linux OS – did not have access to BLE hardware
  Explored the use of BLE dongle – failed to properly work
  iOS Application – appeared simplest to work with and pre-built shells were available

## Slide 14: UI Design
iOS application
  Modified existing Rfduino application code to meet our needs
  Used Xcode Simulator
  Ran the Simulator on a Mac
    Did not have BLE hardware
  Difficulties with acquiring an iOS developer account
    Prevented us from uploading the app onto an iPhone/iPad

## Slide 16: Conclusion
Unfinished tasks
  Test application with BLE capable iOS device
  Finish building and test Printed Circuit Board
  Refine tremor detection algorithm for babies
  Modify device for any conditions specific to individual babies
Lessons learned
  Apple is difficult to work with
  Ensure that you have available equipment to work with your hardware

## Slide 17: Questions?